## Slide 1: What’s in the Duckiebox and how does it work?

## Slide 2: What’s in the box and how does it work?
Content of the Duckiebox
Functionality of each Duckiebot component
Operational fundamentals
A Duckiebox
Jacopo Tani (ETHZ) – first version – 9/22/17
Author name (affiliation) - second version, another date

## Slide 3: Goal
The Duckiebox
The Duckiebot
(in configuration DB17-wjd)

## Slide 4: Duckiebot
Sensing
Actuation
Computation + Memory
Energy
Duckies

## Slide 5: High-level overview
Controller
Sensor
Plant
Actuator
Desired plant input
Input
Output
Measurement
Measurement noise
Reference
path
Disturbances

## Slide 6
Sensor
Actuator
Controller
Computation
Memory
Energy

## Slide 7: Battery Pack
Battery:
Capacity: 10400 mAh
2 outputs @ 4.5 A max (combined)
Input charge @ 2 A
Battery Pack:
Battery
Long USB cable
Short USB cable
Input (charge)
Output (to Raspberry PI and DC Motor HAT)
On/Off (keep pressed) button
Charge Indicator

## Slide 8: Computation and Memory
Bluetooth 4.1 Wi-Fi
2.4 GHz, 802.1n
Composite video and audio output
USB ports
40 Pin GPIO
(General Purpose Input/Output)
LAN port
HDMI output
Power input
up to 2.5A
CSI (Camera Serial Interface) Camera port
Gbps throughput
DSI (Display Serial Interface) display port:
Gbps throughput
Broadcom BCM2837
CPU: 4xARM Cortex-A53, 1.2 GHz
64 bit
1GB LPDDR2 RAM (900 MHz)
GPU: Broadcom VideoCore IV
MicroSD card slot
MicroSD card
16GB
Write: 80 MB/s
Read: MB/s
LAN controller
Heat Sinks

## Slide 9: Computation and Memory: I/Os
Images
Wi-Fi
Power
(from battery)
GPIOs are “batteries” and “switches” at the same time
GPIOs carry signals
Signals can be:
    Power outputs at or
    Ground (reference)
    Digital inputs (Hi-Lo)
    Digital outputs (Hi-Lo)
    Analogue output simulation (PWM)
    Limited current draw for each I/O pin ()
    rail (pin 1 or 17) can output max A, where is the board’s current consumption
Version | Input | Max. total USB draw | Bare board active current consumption (typical) | Camera
3B 1.2 | 2.5A | 1.2A | 400-750 mA | 250 mA
Power consumption figures
Control signal to wheels*

## Slide 10: Chassis Package
Chassis
2x Wheels
1x Omnidirectional (castor) wheel
Mechanical bits (keep the ones you don’t use!)
        Standoffs
        Screws
        Nuts
2x DC motors: Differential drive, each motor independently drives a wheel
1x Screwdriver

## Slide 11: DC Motor
Stator
Rotor
Torque
Angular velocity
Desired plant input
Actual plant input
High level:
Mid level:
Current

## Slide 12: DC Motor – Low level considerations
Notes from the real world:
The Raspberry Pi’s GPIO has only digital outputs can’t provide , only , ;
A similar outcome can be achieved with, Pulse Width Modulation (PWM) of a digital signal;
Motors draw significant currents, Raspberry Pi GPIOs are low-amp and cannot feed them;
GPIOs are connected to the processor. Although protection is in place, back voltage could fry the Pi;
To allow bi-directional wheel motions, a circuit called H-bridge is used. If improperly triggered, it can short circuit and, again, fry the Pi.
extra dedicated hardware: the DC Motor HAT, provides safe and efficient operation
    PWM: Oscillate between , periodically. The smaller the period (), the better.
    Ratio of time spent between and is the duty cycle ()
    Load sees average voltage within period, as if it were a
+ It is easy to build switches (transistors) that do this;
+ It is more power efficient than using an analogue signal
- The PWM frequency must not interfere with the natural dynamics of the controlled load

## Slide 13: DC Motor – Low level
Data (SDA)
Clock (SCL)
3.3V
Ground (reference)
I2C bus
H-bridge
(motor driver)
PWM chip
DC Motor HAT
Power for the motors
Power for the RPI and periphericals

## Slide 14: DC Motor HAT
Motor Drivers
(H-Bridge)
schematics
Power from battery
Motor wires terminal
connectors
Polarity protection FET
PWM chip
GPIO extension
Each motor can draw A @
VDC input
PWM: 8-bit resolution

## Slide 15: Camera
300 mm (long) camera cable
Fisheye lens ( Field of view)
5 MP OV5647 sensor
Max resolution:
1-30 fps @
CCD size:
pixel size
Provides power output
Rolling shutter
S/N ratio:
Dynamic Range: x gain
Camera Mount
CSI port
Power outputs
ProTip: Remove cover before use!

## Slide 16: Tools
Raspberry Pi charger (2.5A)
MicroSD card reader
Zipties
Screwdriver
Universal to CH adapter

## Slide 17: Duckies
A Duckiebot must have at least one Duckie on board

## Slide 18: 5 GHz wireless adapter: the “Edimax”
Provides high-speed Wi-Fi LAN
Great for communicating with laptop and streaming images

## Slide 19: 2.4 GHz wireless joypad
USB Dongle
USB Dongle
Remote control of the Duckiebot
Map functions to buttons during development
Reminder 1: insert batteries
Reminder 2: hardware on/off switch on the back

## Slide 20: External USB drive
32 GB
Read:

## Slide 21: Configurations definition
Let the following hardware be considered “optional”, and be characterized by ():
5 Ghz Wi-Fi adapter “Edimax” (w);
Wireless joypad (j);
External USB drive (d).
The configuration of a Duckiebot is represented by the following notation: DB17-`optional`
`optional` is any of (), in any order.
Examples:
Duckiebot with USB drive, but no wireless adapter: DB17-d
Duckiebot with all optional hardware components: DB17-wjd
Duckiebot with Edimax adapter and joypad, but no USB drive: DB17-jw

## Slide 22: Organization of the lectures/ repo.
0_drafts/: anything goes here. Feel free to make subfolders.
1_beta/: put things here that must be reviewed by others.
2_given/:
  when you give the lecture, save it here with the timestamp and the name of the location.
  Also save a .pdf version.
  These timestamped .key and .pdf files are the ones to be linked to from the class page
  These files are never modified after they are timestamped.
3_ideal/: later, here we will assemble the “ideal” version of the slides.

## Slide 23: Getting the URL to share
Go to Github, click on the file.
On the file page, copy the link that is on the Download button.
They look like this:
  https://github.com/duckietown/lectures/raw/master/duckietown-master.pdf
  https://github.com/duckietown/lectures/raw/master/duckietown-master.key